## Slide 1: Sound Theory
Sound is made up of “pressure waves”
https://astronomy.swin.edu.au/~smaddiso/astro/SiS/NPS/sound1.html
Higher pressure
Lower pressure
Atmospheric pressure
Pressure

## Slide 2: Microphone
Microphone converts sound pressure to voltage
https://astronomy.swin.edu.au/~smaddiso/astro/SiS/NPS/sound1.html
Pressure
Voltage
Mic Output

## Slide 3: Amplifier and A/D
Our mic includes an amplifier
  converts weak voltage to much larger voltage
A/D converts voltage to integer between 0 and 1023
Voltage
Mic Output
Amp
Voltage
Amplifier Output
Arduino A/D
AnalogRead Output
0
511
1023
Gain = 60 dB
Output = 1,000,000 x Input

## Slide 4: Measuring the “Envelope”
Some applications (e.g., speech recognition)
  Need the raw speech waveform (blue)
For other applications (e.g., the “Clapper”)
  We are only interested in the “volume”, AKA “envelope” (red)
1023
:
:
387
:
0
Time
Amplitude
Average amplitude is called the “envelope”
Human Speech

## Slide 5: Standard Averaging
Standard average
  Where xk is the magnitude of the k-th A/D sample
  Slow: not available until N samples measured
  Example:

## Slide 6: Running Average
Also known as the “exponential average”
float avg = 0.
; //larger=smoother
X = analogRead(A0)
Y = |X| //magnitude
loop()
New value of avg consists of:
95% is previous average
5% is new measurement

## Slide 7: Adafruit: “Electret Microphone Amplifier - MAX9814 with Auto Gain Control”
Gain is automatic (not adjustable)
Very sensitive! Gain = 60 dB = 106 = 1,000,000

## Slide 8: Build This
23456 AREF
A0
3.3
220
Louder
Note that we’ll power the microphone using 3.3V rather than 5 V
(less noisy)
Note: AREF pin is connected to 3.3V via the breadboard

## Slide 9
000
001
010
011
100
101
110
111
0 Volts
Default:
Aref = 5 Volts
000
001
010
011
100
101
110
111
0 Volts
3.3 Volts
analogReference:
Aref = 3.3 Volts
000 011 000 001 010
000 101 001 001 100
A/D Output:
A/D Output:


3.3 Volts
5 Volts
Purpose of AREF Pin
Improves A/D resolution for low-voltage microphone signal
  A/D Converter error is proportional to 
analogReference(EXTERNAL) causes the voltage on the AREF pin to be associated with the largest digital value (1032)

## Slide 10: Experiment 1 - Enter this code:
Use Serial Plotter to plot amplitudes
LEDs not used in this sketch
Use this when AREF pin used
Otherwise, default is 5V

## Slide 11: Experiment 2: Average Volume
Try these experiments:
Change ‘alpha’ to 0.99
Change ‘alpha’ to 0.15
Watch Serial Plotter
Understand output

## Slide 12: Make an LED Light Gauge
Add logic to make the LEDs change with volume
  Higher sound lights up more LEDs
  You already have the circuit
Changes required
  Define volume threshold to light up each LED
  Add pinMode statements to setup()
  Add digitalWrite statements to loop()

## Slide 13: LED Thresholds
If avgVol > 20 turn on first LED: requires very little sound
if avgVol > 40 also turn on second LED:
and so on. Very subjective – adjust as desired

## Slide 14: Modify setup()
We need to declare LED pins (2-6) to be OUTPUT
  Can do them all using one ‘for’ loop:

## Slide 15: Modify loop()
Many ways to do this – one way is to check threshold for each LED

## Slide 16: Experiment
Upload and activate Serial Plotter
Try different thresholds
  Make it more or less sensitive
Try different alpha values
  Make it quicker or slower to respond

## Slide 17: Display Sound Volume in Decibels
In class if we have time
Do at home if we don’t

## Slide 18: Decibels – how the Pro’s do it
Sound pressure level is often represented as decibels (dB) dB
  In acoustics, ref is the threshold of hearing, .00002 Pascals
Logarithm is a good model of human hearing
  When spl is doubled it adds about 6 dB to L
Our system has not been calibrated for ‘ref’
  i.e., Our result is off by an unknown constant
  Measured dB = True dB + Unknown Constant
Therefore, we use a Pot to adjust the thresholds
  New LED threshold = Old threshold + potValue
  We’ll call the variable name basedB instead of potValue
0 dB: softest hearable sound
30 dB: soft whisper
40-50 dB: office
60 dB: normal conversation
70 dB: TV audio
80-90 dB: blender
110 dB: crying baby, rock concert
130 dB: chain saw, jack hammer
120-140 dB: Pain threshold

## Slide 19
Pot sets baseline dB value:
Adjust so that LEDs are all turned off in ambient noise

## Slide 20: Decibel Program
What changes?
LED Thresholds are in dB
  Each 6 dB is doubling of sound intensity
On Serial Plotter, notice that dB values are less sensitive than raw volume changes. That’s how the ear works!
Unadjusted Thresholds

## Slide 21: Other Software Changes

## Slide 22: Adjustment
Adjust pot so ambient noise does not trigger LEDs (about 60 dB)
Each LED represents additional 6 dB
basedB set by Potentiometer
Ambient Noise
LEDs are ON

## Slide 23: Arduino Output Sounds
Suppose we turn on and off an Arduino pin
  And connect pin to a speaker
  What do we get?
.5ms
1ms
Time
HIGH
LOW
2ms
pop
pop
pop
pop
pop
3ms
4ms
“Buzz” sound with “pitch” frequency F = 1000 Hz
500𝜇s
1000𝜇s
2000𝜇s
3000𝜇s

## Slide 24: Generating a Buzz
Arduino Sketch to generate 1000 Hz buzz:
    int BUZpin=8; //speaker connected to pin 8
    loop(){
  digitalWrite(BUZpin, HIGH);
  delay(.5);
  digitalWrite(BUZpin, LOW);
  delay(.5);
  }
Problem: delay values must be integers
  Cannot use “.5”
HIGH
LOW
delay
delay
BUZpin Output
.5ms 1ms 1.5ms 2ms
delay
Just like the BLINK program!

## Slide 25: delayMicroseconds(d)
Suppose we want F=1000 pulses per sec (1 kHz)
Time per pulse T = 1/F = 1/1000 =1 ms = 1000 s (microseconds)
Time between pulses = T/2 = .5 ms = 500 s
delay(.5); won’t work! Fraction delays not allowed.
delayMicroseconds(500) does work

## Slide 26: Active Buzzer Vs Passive Buzzer
Active buzzer
  When you apply constant 5V, it emits a continuous tone, which is automatically generated by its built-in electronics. Nice for using in a Morse code generator.
Passive buzzer
  Inside the canister a membrane moves out or in depending on applied voltage.
    Apply constant 5V: membrane moves out and stays there. You might hear a click noise, but no continuous sound is generated
    Apply a voltage that is alternately turned on and off; this causes the membrane to move in and out, which generates a sound (“buzz”). This is exactly how the speaker in your TV or cell phone works.
  The pitch of the buzzer is controlled by how fast we change the voltage. Arduino’s “Tone” command automatically generates any desired frequency.
Active Buzzer
(black bottom)
Passive Buzzer
Acts like speaker
(green bottom)

## Slide 27: Buzzer Sketch
Type the following into a new sketch
  You don’t have to type the comments

## Slide 28: Build This (Just add buzzer to your current breadboard circuit)
Find your passive buzzer
  Has green bottom
  Careful! It’s polarized
    Buzzer has + and -
Upload your buzzer sketch

## Slide 29: How to be less annoying
It gets pretty bad when 20 people are playing a buzzer.
To quiet your buzzer:
  Unplug it
  OR
  Upload the empty sketch

## Slide 30: Challenges
Modify to play a 250 Hz tone
  Solution: Each pulse duration T = 1/250 s
  Gives T=.004 Sec = 4000 microseconds
  Gap between pulses is T/2 = 2000 microseconds
  Change delays to: delayMicroseconds(2000)
Modify to play 100 Hz and 3000 Hz
  T = 1/100 and T/2 = 1/200 = ? microseconds
  T = 1/3000 and T/2 = 1/6000 = ? microseconds
Notes: For 3000, T = 1000000/3000 = 333. delayM = 333/2 = 167 us
For 100, T=1000000/100 = 10000. delayM = 10000/2 = 5000 us
For 800, T=1000000/800 = 1250. delayM = 625 us

## Slide 31: How to generate 1 Sec buzz
  int t0=millis(); //get starting time in ms
  while (millis()-t0<1000){ //make buzzer sound for 1000 ms
  …write buzzer pin HIGH
  …write buzzer pin LOW
  }
  delay(1000); //stay off for a second
millis() returns the number of milliseconds since Arduino power-up
millis()-t0 gives elapsed time since step 1
  while loop runs until elapsed time > 1000 ms
Notes: void loop() {
//this part makes buzzer turn on for 1 sec every 5 sec
long int t0 = millis();
while (millis() - t0 < 250) {
digitalWrite(buzzPin, HIGH); // turn the LED on (HIGH is the voltage level)
delayMicroseconds(delayM); // wait
digitalWrite(buzzPin, LOW); // turn the LED off by making the voltage LOW
delayMicroseconds(delayM); // wait
}
delay(250);
delayM = delayM + 100;
if (delayM > 3000) delayM = 100;
}

## Slide 32: Please Solve These Challenges
Challenge #1
  Make your buzzer buzz for 0.25 second
  Then stay off 0.25 seconds
  Repeat forever
Challenge #2
  Modify Challenge #1 code so that delayM is initialized to 100
  Each time it buzzes, delayM increases by 100
  If delayM exceeds 3000, reset to 100

## Slide 33: Arduino Music
Why?
Define statements
Arrays
More Functions

## Slide 34: Play a tune
Examples -> Digital -> toneMelody
Push red “reset” button to replay
Let’s look at the new things Please have the toneMelody sketch displayed on your screen

## Slide 35: “Tone” statement
Syntax tone(pin, frequency) tone(pin, frequency, duration)
E.g., tone(8,500)
  plays 500 Hz tone on pin 8
  Must be stopped using noTone(8) statement
E.g., tone(8,500,1000)
  plays 500 Hz tone for 1 second on pin 8

## Slide 36: Define Statements
Example:
  #define AlarmPin 8 //pin number for LED1
  #define longdelay 100 //# ms to delay
  pinMode(AlarmPin, OUTPUT);
  delay(longdelay);
Same as:
  pinMode(8, OUTPUT);
  delay(100);
Similar to:
int AlarmPin=8;
int longdelay=100;
Advantage: #define doesn’t use memory for variable storage

## Slide 37: pitches.h is a “header file”
Click on pitches.h tab
equivalent ways to play 41 Hz tone:
tone(8,41)
tone(8,NOTE_E1)
Etc., etc.
Include statement in toneMelody:

## Slide 38: “Array”
An Array is just a list of values
The first note in the song is: melody[0]=NOTE_C4
The second note is: melody[1] =NOTE_G3
The k-th note is: melody[k-1]

## Slide 39: Array Example
int LEDPins[] = {5, 7, 10, 8}; //LEDs connected to pins 5,7,8,10
void setup(){
for (int k=0; k<4; k++){
pinMode(LEDPins[k], OUTPUT);
}
This is same as the following:
pinMode(5, OUTPUT); //since LEDPins[0] = 5
pinMode(7, OUTPUT); //since LEDPins[1] = 7
pinMode(8, OUTPUT); //since LEDPins[2] = 10
pinMode(10, OUTPUT); //since LEDPins[3] = 8

## Slide 40: toneMelody walk-through
void setup() {
for (int thisNote = 0; thisNote < 8; thisNote++) {
//e.g. quarter note = 1000 / 4, eighth note = 1000/8, etc.
int noteDuration = 1000 / noteDurations[thisNote];
tone(8, melody[thisNote], noteDuration);
// to distinguish the notes, set a minimum time between them.
int pauseBetweenNotes = noteDuration * 1.30;
delay(pauseBetweenNotes);
// stop the tone playing:
noTone(8);
}
}
Why does it play tune only once???
Push RESET to replay

## Slide 41: Another Code Example
Load playSong1.ino
Changes made:
  Plays song in loop() rather than setup()
    Song repeats over and over
  Detects end of song automatically (without needing to count exact number of notes)
  Can adjust how fast song plays

## Slide 42: Detecting End of Song
Add a zero as last item in duration array
For loop goes until zero detected: for (int thisNote = 0; JepardyDurations[thisNote] != 0; thisNote++) {

## Slide 43: Change Pace of Music
Find the line: int wholeNote = 1000;
  ‘wholeNote’ is the number of milliseconds in a whole note.
Changing wholeNote to 500 makes whole note ½ sec
Changing wholeNote to 2000 makes whole note 2 sec
Please try several values for wholeNote and see what happens

## Slide 44: Optional Material
The following material (approximately 10 slides) on Arduino music is optional and will not be on a test.
However, you might find it useful to work through it if you have time

## Slide 45: Multiple Songs
Load playSong3
Changes:
  Three songs available
  Uses a function to play the melody
  Variable “song” set to 0, 1, or 2 to select song.
    Find the line: int song = 0;
    Change song to 0, 1, or 2 to select the melody

## Slide 46: Look at loop()
    int wholeNote = 1450; // change pace of music("speedy")
    int song = 0; //select a song (set to 0, 1, or 2)
    void loop() {
    if (song == 0) {
    singsong(marioDurations, Mario); //play Mario
    }
    else if (song == 1) {
    singsong(BondDurations, Bond); //play James Bond
    }
    else {
    singsong(JepardyDurations, Jepardy); //play Jepardy
    }
    }

## Slide 47: Look at singsong()
Shows how to pass values to function
Shows how to re-use code
  Same code can play many different tunes

## Slide 48: Whistles and Bells Mods to playSong3
Pushbutton Select
Pace adjustment

## Slide 49: Add: Pot and Switch
A0
Gnd +5
Add This
(adjusts pace)
Add This
(selects song)
Potentiometer
“Pot”

## Slide 50: Code Modifications
Where do these go?
int switchPin=12; //pushbutton pin
int potPin=A0; //pin that pot is connected to
int song = 0; //which song to play
int nsong = 3; //# songs
Where does this go?
pinMode(switchPin,INPUT_PULLUP)

## Slide 51
Code to select song. Where does it go?
    if (digitalRead(switchPin) == LOW) {
    song = (song + 1) % nsong;
    delay(1000); //wait a polite second
    return;
    }
What does it do?
  digitalRead goes LOW when button pressed
  “%” is modulo division by nsong=3
  song stays in range: 0  song  2
Notes: This goes in singsong function, within for loop

## Slide 52: Modifications Continued
Code to modify pace. Where does it go?
  wholeNote = analogRead(potPin) * 3; //read the pot setting
What does it do?
  Remember: wholeNote is length of whole note (in ms)
  And recall: analogRead value is 0  x  1023
  Therefore: 0  wholeNote  3069
  And So: whole notes range from 0 to 3.069 sec

## Slide 53: Try it
Put these changes in yourself
  You’ll have to figure out where they go
(OR just load the complete program)
  playSongExtras.ino

## Slide 54: Challenges
Get a melody off the internet and add it to sketch
  Sometimes they are already in Arduino format
  Sometimes you have to transcribe the notes
  Changes required
    Add two arrays: melody and duration
    Add code to play the new song inside loop()
    Make nsong equal to # songs
Add 3 or more LEDs to show frequency of each tone
  if (mel[thisNote] < 200) light LED #1 //You have to write else if (mel[thisNote]<800) light LED #2 //this in proper C code! else light LED #3