## Slide 1: Day 8
Using Arduino to Make “Music”
(not great music, but music none the less)

## Slide 2: Arduino Output Sounds
Suppose we turn on and off an Arduino pin
  And connect pin to a speaker
  What do we get?
.5ms
1ms
Time
HIGH
LOW
2ms
pop
pop
pop
pop
pop
3ms
4ms
“Buzz” sound with “pitch” frequency F = 1000 Hz
500𝜇s
1000𝜇s
2000𝜇s
3000𝜇s

## Slide 3: Generating a Buzz
Arduino Sketch to generate 1000 Hz buzz:
    int BUZpin=8; //speaker connected to pin 8
    loop(){
  digitalWrite(BUZpin, HIGH);
  delay(.5);
  digitalWrite(BUZpin, LOW);
  delay(.5);
  }
Problem: delay values must be integers
  Cannot use “.5”
HIGH
LOW
delay
delay
BUZpin Output
.5ms 1ms 1.5ms 2ms
delay
Just like the BLINK program!

## Slide 4: delayMicroseconds(d)
delay(.5); won’t work! Fraction delays not allowed.
Time between pulses = T/2 = .5 ms = 500 s
delayMicroseconds(500) does work

## Slide 5: Active Buzzer Vs Passive Buzzer
Active buzzer
  Apply constant 5V, it emits a continuous tone
  Automatically generated by its built-in electronics.
Passive buzzer
  A membrane moves out or in depending on applied voltage.
    Constant 5V: membrane moves out and stays there. No continuous sound is generated
    Voltage switched on and off: membrane moves in and out, which generates a sound (“buzz”).
  Pitch frequency is controlled by how fast we change the voltage.
Active Buzzer
(black bottom)
Passive Buzzer
Acts like speaker
(green bottom)

## Slide 6: Buzzer Sketch
Type the following into a new sketch
  You don’t have to type the comments

## Slide 7: Build This (Just add buzzer to your current breadboard circuit)
Find your passive buzzer
  Has green bottom
  Careful! It’s polarized
    Buzzer has + and -
Upload your buzzer sketch

## Slide 8: How to be less annoying
It gets pretty bad when 20 people are playing a buzzer.
To quiet your buzzer:
  Unplug it
  OR
  Upload the empty sketch

## Slide 9: Challenges
Modify to play a 250 Hz tone
  Solution: Each pulse duration T = 1/250 s
  Gives T=.004 Sec = 4000 microseconds
  Gap between pulses is T/2 = 2000 microseconds
  Change delays to: delayMicroseconds(2000)
Modify to play 100 Hz and 3000 Hz
  T = 1/100 and T/2 = 1/200 = ? microseconds
  T = 1/3000 and T/2 = 1/6000 = ? microseconds
Notes: For 3000, T = 1000000/3000 = 333. delayM = 333/2 = 167 us
For 100, T=1000000/100 = 10000. delayM = 10000/2 = 5000 us
For 800, T=1000000/800 = 1250. delayM = 625 us

## Slide 10: How to generate 1 Sec buzz
  int t0=millis(); //get starting time in ms
  while (millis()-t0<1000){ //make buzzer sound for 1000 ms
  …write buzzer pin HIGH
  …write buzzer pin LOW
  }
  delay(1000); //stay off for a second
millis() returns the number of milliseconds since Arduino power-up
millis()-t0 gives elapsed time since step 1
  while loop runs until elapsed time > 1000 ms
Notes: void loop() {
//this part makes buzzer turn on for 1 sec every 5 sec
long int t0 = millis();
while (millis() - t0 < 250) {
digitalWrite(buzzPin, HIGH); // turn the LED on (HIGH is the voltage level)
delayMicroseconds(delayM); // wait
digitalWrite(buzzPin, LOW); // turn the LED off by making the voltage LOW
delayMicroseconds(delayM); // wait
}
delay(250);
delayM = delayM + 100;
if (delayM > 3000) delayM = 100;
}

## Slide 11: Solve These Challenges
Challenge #1
  Make your buzzer buzz for 0.25 second
  Then stay off 0.25 seconds
  Repeat forever
Challenge #2
  Modify Challenge #1 code so that delayM (time between pulses) is initialized to 100
  Each time it buzzes (every .25 sec), delayM increases by 100
  If delayM exceeds 3000, reset to 100

## Slide 12: Arduino Music
Why?
Define statements
Arrays
More Functions

## Slide 13: Play a tune
Examples -> Digital -> toneMelody
Push red “reset” button to replay
Let’s look at the new things Please have the toneMelody sketch displayed on your screen

## Slide 14: “Tone” statement
Syntax tone(pin, frequency) tone(pin, frequency, duration)
E.g., tone(8,500)
  plays 500 Hz tone on pin 8
  Must be stopped using noTone(8) statement
E.g., tone(8,500,1000)
  plays 500 Hz tone for 1 second on pin 8

## Slide 15: “Define” Statements in C
Example:
  #define AlarmPin 8 //pin number for LED1
  #define longdelay 100 //# ms to delay
  pinMode(AlarmPin, OUTPUT);
  delay(longdelay);
Same as:
  pinMode(8, OUTPUT);
  delay(100);
Similar to:
int AlarmPin=8;
int longdelay=100;
Advantage: #define doesn’t use memory for variable storage

## Slide 16: pitches.h is a “header file” (stored in the same directory)
Click on pitches.h tab
equivalent ways to play 41 Hz tone:
tone(8,41)
tone(8,NOTE_E1)
Etc., etc.
Include statement in toneMelody:

## Slide 17: “Array”
An Array is just a list of values
The first note in the song is: melody[0]=NOTE_C4
The second note is: melody[1] =NOTE_G3
The k-th note is: melody[k-1]

## Slide 18: Array Example
int LEDPins[] = {5, 7, 10, 8}; //LEDs connected to pins 5,7,8,10
void setup(){
for (int k=0; k<4; k++){
pinMode(LEDPins[k], OUTPUT);
}
This is same as the following:
pinMode(5, OUTPUT); //since LEDPins[0] = 5
pinMode(7, OUTPUT); //since LEDPins[1] = 7
pinMode(8, OUTPUT); //since LEDPins[2] = 10
pinMode(10, OUTPUT); //since LEDPins[3] = 8

## Slide 19: toneMelody walk-through
void setup() {
for (int thisNote = 0; thisNote < 8; thisNote++) {
//e.g. quarter note = 1000 / 4, eighth note = 1000/8, etc.
int noteDuration = 1000 / noteDurations[thisNote];
tone(8, melody[thisNote], noteDuration);
// to distinguish the notes, set a minimum time between them.
int pauseBetweenNotes = noteDuration * 1.30;
delay(pauseBetweenNotes);
// stop the tone playing:
noTone(8);
}
}
Why does it play tune only once???
Push RESET to replay

## Slide 20: Another Code Example
Load playSong1.ino
Changes made:
  Plays song in loop() rather than setup()
    Song repeats over and over
  Detects end of song automatically (without needing to count exact number of notes)
  Can adjust how fast song plays

## Slide 21: Detecting End of Song
Add a zero as last item in duration array
For loop goes until zero detected:

## Slide 22: Change Pace of Music
Find the line: int wholeNote = 1000;
  ‘wholeNote’ is the number of milliseconds in a whole note.
Changing wholeNote to 500 makes whole note ½ sec
Changing wholeNote to 2000 makes whole note 2 sec
Please try several values for wholeNote and see what happens

## Slide 23: Optional Material
If you have time

## Slide 24: Multiple Songs
Load playSong3
Changes:
  Three songs available
  Uses a function to play the melody
  Variable “song” set to 0, 1, or 2 to select song.
    Find the line: int song = 0;
    Change song to 0, 1, or 2 to select the melody

## Slide 25: Look at loop()
    int wholeNote = 1450; // change pace of music("speedy")
    int song = 0; //select a song (set to 0, 1, or 2)
    void loop() {
    if (song == 0) {
    singsong(marioDurations, Mario); //play Mario
    }
    else if (song == 1) {
    singsong(BondDurations, Bond); //play James Bond
    }
    else {
    singsong(JepardyDurations, Jepardy); //play Jepardy
    }
    }

## Slide 26: Look at singsong()
Shows how to pass values to function
Shows how to re-use code
  Same code can play many different tunes

## Slide 27: Whistles and Bells Mods to playSong3
Pushbutton Select
Pace adjustment

## Slide 28: Add: Pot and Switch
A0
Gnd +5
Add This
(adjusts pace)
Add This
(selects song)
Potentiometer
“Pot”

## Slide 29: Code Modifications
Where do these statements go?
Where does this go?

## Slide 30
Code to select song. Where does it go?
What does it do?
  digitalRead goes LOW when button pressed
  “%” is modulo division by nsong=3
  song stays in range: 0  song  2
Notes: This goes in singsong function, within for loop

## Slide 31: Modifications Continued
Code to modify pace. Where does it go?
What does it do?
  Remember: wholeNote is length of whole note (in ms)
  And recall: analogRead value is 0  x  1023
  Therefore: 0  wholeNote  3069
  And So: whole notes range from 0 to 3.069 sec

## Slide 32: Try it
Put these changes in yourself
  You’ll have to figure out where they go
(OR just load the complete program)
  playSongExtras.ino

## Slide 33: Challenges
Get a melody off the internet and add it to sketch
  Sometimes they are already in Arduino format
  Sometimes you have to transcribe the notes
  Changes required
    Add two arrays: melody and duration
    Add code to play the new song inside loop()
    Make nsong equal to # songs
Add 3 or more LEDs to show frequency of each tone
  if (mel[thisNote] < 200) light LED #1 //You have to write else if (mel[thisNote]<800) light LED #2 //this in proper C code! else light LED #3